## Slide 1: Remote Satellite Ground Station
KE8HMV
ansofive@gmail.com
Dennis “Too Much Time On My Hands” Dunn

## Slide 2
The Problem:
  No money to buy low-loss coax cable to connect an outdoor antenna to an SDR.
  A desire to participate in ham radio satellite contacts.
  No career to occupy my time.
The Solution:
  A Docker engine running on Raspberry Pi co-located with the antenna. The hardware is powered by passive power-over-Ethernet which also provides network connectivity.
  The containers provide various services to the station operator.
  Reception of signals is provided by a software-defined-radio.
  Transmission of a signal is provided by a handheld transceiver.

## Slide 3
Satellite prediction service
Satellite prediction REST API
SDR control REST API
Trx interface service
UI
Icecast
Icecast source
SDR control service
Icecast source
Docker engine
Container
Container

## Slide 4
Satellite prediction service
  kd2bd/predict running in server mode
Satellite prediction service REST API
  Maps REST calls to UDP control packets
SDR control service
  sysrun/rtl-sdr rtl_fm
SDR control service REST API
  Maps REST calls to UDP control packets
Trx interface service
  Interfaces a Baofeng UV-5R handheld transceiver to audio streams
Icecast
  Creates streams of the rtl_fm audio output and UI mic input
UI
  A react application